## Slide 1: Signal and Noise in Measurement Systems
Sensors and Actuators – Joel von Rotz

## Slide 2: Overview
Signal Types
Statistical Representation of random signals
Effects of noise and interference on measurement circuits
Noise sources and coupling mechanisms
Methods of reducing effects of noise and interference

## Slide 3: Determenistic & Random
Notes: Output signals, for example a step or sine wave, are deterministic signals, since after enough observation (one period), the signal can be predicted at any future point of time.
Input signals are viewed as random, since the format of an input signal is unknown, hence the measured signal can’t be extrapolated at any future point of time.

## Slide 4: Statistical Representation of Random Signals
Notes: Since the signal is random, it can’t be expressed as a continuous function. The measuring is done in discreet steps (when using microcontrollers) and therefore the signal is expressed as a series of values . Using these values, the probability of signals can be calculated.
Since the signal is random, it can’t be expressed as a continuous function. The measuring is done in discreet steps (when using microcontrollers) and therefore the signal is expressed as a series of values 𝑦[𝑘]. Using these values, the probability of signals can be calculated.

## Slide 5: Mean
Standard Deviation
Case :
Notes: Since the signal is random, it can’t be expressed as a continuous function. The measuring is done in discreet steps (when using microcontrollers) and therefore the signal is expressed as a series of values . Using these values, the probability of signals can be calculated.
Since the signal is random, it can’t be expressed as a continuous function. The measuring is done in discreet steps (when using microcontrollers) and therefore the signal is expressed as a series of values 𝑦[𝑘]. Using these values, the probability of signals can be calculated.

## Slide 6: Probability Density Function Statistical Representation of Random Signals
Probability
Cumulative Probability & Cumu. Prob. Dist. Function
Notes: Probability (: total sample : amount of samples in th section)
Probability 𝑃_𝑗=𝑛_𝑗/𝑁 (𝑁: total sample 𝑛_𝑗: amount of samples in 𝑗th section)

## Slide 7: Normal Probability Density Function Statistical Representation of Random Signals
Notes: For the distribution of amplitude signals, the normal probability distribution function is sufficient.

## Slide 8: Probability Density Function Statistical Representation of Random Signals
Notes: The probability function is check what the probability is, that a signal is in a certain range. This way the general behaviour of the system can be checked. If there are signals outside the range, the system can be adjusted to reduce the error.

## Slide 9: Power Spectral Density Statistical Representation of Random Signals
Notes: The power of a signal, which is measured over a period of , is used to quantify random signals.
It is stationary, meaning that the value won’t change over time, while the signal recordings can look differently.
The squared average of a signal is equal to the average power.
Power spectral density is a stationary quantity which is a measure of how the power in a random signal is distributed amongst these different frequencies.
The power of a signal, which is measured over a period of 𝑇_0, is used to quantify random signals.
It is stationary, meaning that the value won’t change over time, while the signal recordings can look differently.
The squared average of a signal is equal to the average power.
Power spectral density is a stationary quantity which is a measure of how the power in a random signal is distributed amongst these different frequencies.

## Slide 10: Power Spectral Density Statistical Representation of Random Signals
Total Power
Cumulative Power (c.p.f)
Power Spectral Density
Notes: The power of a signal, which is measured over a period of , is used to quantify random signals.
It is stationary (when the signal is also stationary over its period), meaning that the value won’t change over time, while the signal recordings can look differently.
The squared average of a signal is equal to the average power + using the fourier series, the signal’s power is distributed across the spectrum.
Power spectral density is a stationary quantity which is a measure of how the power in a random signal is distributed amongst these different frequencies.
The power of a signal, which is measured over a period of 𝑇_0, is used to quantify random signals.
It is stationary (when the signal is also stationary over its period), meaning that the value won’t change over time, while the signal recordings can look differently.
The squared average of a signal is equal to the average power + using the fourier series, the signal’s power is distributed across the spectrum.
Power spectral density is a stationary quantity which is a measure of how the power in a random signal is distributed amongst these different frequencies.

## Slide 11: Power Spectral Density Statistical Representation of Random Signals
White Noise (internal noise)
Band Limited White Noise (noise and signal)
Notes: White noise, which is internal noise in electronics, can be represented as a constant amplitude over
Band Limited White Noise is good for representing noise and measurement signals!  cut off frequency

## Slide 12: Autocorrelation Statistical Representation of Random Signals
Notes: Autocorrelation can be used to calculate delays between an input and output of a system.
The autocorrelation has the same frequency as the signal itself!

## Slide 13: Autocorrelation Statistical Representation of Random Signals
Detecting Periodicity
Estimating Signal Properties
https://pages.mtu.edu/~suits/autocorrelation.html
Notes: Autocorrelation can be used to calculate delays between an input and output of a system.
The autocorrelation function of any periodic signal has the same period as the signal itself
Usage
  Find period of signal by analysing peaks
  Find rms value by setting delay to 0

## Slide 14: Autocorrelation Statistical Representation of Random Signals
Notes: Autocorrelation can be used to calculate delays between an input and output of a system.
The autocorrelation function of any periodic signal has the same period as the signal itself

## Slide 15: Voltage transmission – series mode interference Effects of noise and interference on measurement circuits

## Slide 16: Current transmission – series mode interference Effects of noise and interference on measurement circuits

## Slide 17: Voltage transmission – common mode interference Effects of noise and interference on measurement circuits

## Slide 18: Signal to Noise Ratio (SNR) Effects of noise and interference on measurement circuits
Notes: All values are in RMS

## Slide 19: Noise Sources
Thermal/Johnson Noise – Uniform over all spectrum
Noise in resistors and semiconductors. Modelled as white Gaussian noise.
Shot Noise (Occurs in Transistors)
Occurs in transistors and often modelled as white noise.
Notes: Thermal noise is

## Slide 20: External Noise Sources
AC Sources – most common interference
for example 230V, 50Hz
DC Sources – Switching signals, impulses
RFI – Radio frequency from oscillators
Notes: AC Sources are the most common type of interferences, as the changing signals influence measurement circuits and nearby circuits. A good example is 230V + 50Hz (main power)
DC Sources themselves don’t interfere with circuits (except for maybe electrical fields), but the changing states of these DC signals create interferences.
RFI: oscillators in radio frequency transmitters and receivers  can get picked up by nearby circuits of the system

## Slide 21: Inductive Coupling Coupling Mechanism
Notes: M: Mutual inductance

## Slide 22: Capacitive Coupling Coupling Mechanism
Notes: No interference when C1=C2, C1e=C2e

## Slide 23: Multiple Earths Coupling Mechanism

## Slide 24: Noise Reduction Methods
Physical separation
Electromagnetic Shielding (e.g. twisted cables)
Electrostatic Screening and Shielding
Differential amplifiers (e.g. Low noise amplifier, current sense amplifier)
Filtering (e.g. noise filtering using a bandpass)
Modulation
Averaging repetitive signal ()
Autocorrelation to detect presence of periodic signal in buried in random noise